## Slide 1: Introducing the Trimble® X7

## Slide 2: Trimble X7 3D Laser Scanner
Simple
  Exceptional innovations that boost user confidence and ease of use
Smart
  Breakthrough technology and features deliver precise, efficient in-field data collection empowering users
Professional
  Instrument and data quality you can trust
  Complete workflows to drive efficiency and reduce downtime
A well balanced solution for effective performance in the field

## Slide 3: Trimble X7 Key Messages
Simple
  Reliable field workflows suitable for all users
  Intuitive Perspective software to operate, manage, view and validate scan data
  Fast image capture with Trimble VISION™ technology
  Compact and lightweight for easier transport and mobility

## Slide 4: Trimble X7 Key Messages
Smart
  Breakthrough innovations for reliable data collection
  New Trimble X-Drive enables automatic calibration to ensure accuracy on every scan and reduce downtime.
  Trimble Registration Assist for full automatic registration, refinement and reporting to leave the site with confidence.
  Automatic survey grade level compensation
  Flexible operation with tablet or one-button workflow

## Slide 5: Trimble X7 Value Proposition
Professional
  Reliable IP55 rating
  Industry leading 2-year warranty
  High sensitivity time-of-flight EDM to effectively capture dark and reflective surfaces
  Full data redundancy onboard SD card and on Tablet
  Data integration with Trimble and non-Trimble software
  Operating temperatures -20°C → +50°C

## Slide 6: X7 Technical Overview
Speed, Spacing, Duration, Points
Digital Time of Flight EDM
360° x 282° FOV
Scan Duration
  1:34 - 14:57 min:sec
Point Spacing
  3.5 - 11.4mm @ 10m
Number of Points/Scan
    12 - 125 million
500kHz or 166kHz
Environmental
  IP55
  Operating Temperature
    -20°C to +50°C (-4°F to 122°F)
  5.8kg (including battery)
  2-year Warranty
VISION
  3 integrated cameras
  Speed: Fast 1 min - Quality 2 min
  Resolution: Fast 158 MP - Quality 316 MP
Features
  Automatic Calibration
  Trimble Registration Assist
  Survey Grade Self Leveling
    3” accuracy
Measurement Range
  0.6m - 80m
Accuracy
  3D point accuracy
    3.5mm @ 20m
  Range Noise
  <3mm @ 60m on 80% albedo
Communications
  Dual Band WiFi
  USB cable

## Slide 7: Trimble X7 System Overview
Trimble X7 System
  Trimble X7 3D Laser Scanner
  Trimble Perspective Field Software
  Custom Gitzo Series 3 Tripod
  Custom Gitzo QR adapter
  Custom Trimble Backpack
Additional System Components
  Standard Trimble optical battery
  Trimble RealWorks® and Trimble Business Center
High-speed 3D laser scanning system with new innovations to simplify adoption, increase efficiency and provide confidence in the field.

## Slide 8
Trimble X7 Key Features

## Slide 9: Smart - Trimble X-Drive
World’s first dual vertical deflection scanning drive system integrating…
  Survey-grade servo drive +
  High speed laser scanning
  Smart co-axial camera system
All in a protected center unit to enable…
  First-ever auto-calibrating laser scanner
  Productive image capture
  Minimized parallax between scans and images

## Slide 10: Smart - Trimble X-Drive: Auto Calibration
25 second Auto-calibration without targets
Ensure data accuracy on every scan
SMART calibration monitors instrument and environmental change to optimize the calibration process
Eliminate downtime from annual calibration service
Reduces maintenance cost
Lowers overall cost of ownership
Enables 2 year standard warranty

## Slide 11: Simple - Trimble Perspective
Trimble Perspective Software, 3D scanning simplified
  easy to adopt for new users
  sophisticated control for experts
Intuitive user interface
3D data visualization
Automated Registration
Annotation and measurement
Seamless data integration

## Slide 12: Smart - Automated Registration
Trimble Registration Assist
Automated IMU based registration
  Register in the field to save time in the office
  Ensure data is complete and correct before you leave the project site
  Avoid costly rework and additional site revisits
Notes: One of the most powerful features of Trimble Perspective Software is the Trimble Registration Assist. Combined with the scanners IMU, Trimble Registration Assist will automatically register scans as the are acquired. By default it will attempt to register to the previous scan. However, you may find that you need to move around your project in such a way that you may not be close to the last scan. In this case the software allows you to select which scan station you would like to register to. In the case that you don’t have an overlapping scan to register to Trimble Registration Assist will create a registration group which you can then register later.

## Slide 13: Professional - Labels and Annotations
Ensure field productivity, while ensuring data quality and accuracy
Document to control registration and project orientation
Help office personnel understand the scene
Available in both 3D and Station-based views

## Slide 14: Measurement Types
Make decisions in the field
Constrained
Horizontal - station view only
Vertical - station view only
Area - top view only
Unconstrained
Single point coordinates - all views
Point to point - top view, side view, or station view
Notes: Single point coordinate x,y,z from 3D, locked top/side view or station view
Point to Point measurement - locked top/side view or station view
Area - locked top view
constrained z clearance - station view only
constrained point to point in XY plane - station view only

## Slide 15: Digital Time of Flight EDM
Standard 500kHz
High Sensitivity mode 166kHz
Minimum range 0.6m
Maximum range 80m
Range accuracy 2mm
Range noise
  <3mm @ 60m on 80% albedo
Field of view
  360° x 282°
Capture difficult surfaces
  Dark
  Reflective
  Shiny

## Slide 16: Simple - Scan Duration and Spacing
Standard (STD) - simple, short range or light surfaces
High Sensitivity (HS) - complex, long range or dark surfaces
1 - Duration is rounded up to the nearest minute and includes longest calibration time
Duration1 (Min) | Scan Mode | Spacing (mm) @ 10m | Spacing (mm) @ 35m | Spacing (mm) @ 50m | Number of Points (Mpts) | Max File Size (MB)
2 | Standard | 11 | 40 | 57 | 12 | 160
4 | Standard | 5 | 18 | 26 | 58 | 420
 | High Sensitivity | 9 | 33 | 47 | 17 | 190
7 | Standard | 4 | 12 | 18 | 125 | 760
 | High Sensitivity | 6 | 21 | 30 | 42 | 330
15 | High Sensitivity | 4 | 13 | 19 | 109 | 710

## Slide 17: Smart - Trimble VISION 360
3 Coaxial 10MP integrated cameras
Fast image capture
  Fast 15 images (6 positions) in 1 min
  Quality 30 images (12 positions) in 2 min
360° x 282° FOV
  Fast mode 158 MP (Raw data capture)
  Quality mode 316 MP (Raw data capture)
White Balance
  Indoor and Outdoor Presets
  Auto
Notes: KEY: THIS DOESN’T INCREASE THE MPX RESOLUTION OF THE PANO. THE PANO IS 65MP EITHER WAY!

## Slide 18: Smart - Trimble VISION 360
Fast, clear color imagery
  Full field of view panoramas
  Colorized point clouds

## Slide 19: Smart - Panorama Creation
Fast & Quality Panorama creation
Fast in-field Panorama creation
  Uses fixed distance to minimize mismatches
  No blending or occlusion correction
  Better for simple scenes
  Fast to preserve battery power
Quality export panorama creation
  Uses the real pointcloud distance to minimize mismatches.
  Better on complex scenes
  Blending to smooth discontinuities between images
  Quality to give the best customer experience

## Slide 20: Smart - Automatic Level Compensation
No compromise between accuracy and Productivity
Survey-grade accuracy < 3 arc seconds within ±5°
  Level accuracy on setups > ±5°
Working range up to 45° tilt for coarse leveling
Automates field workflows to reduce error and save time
Less field expertise required
User configurable On/Off
  Note: Off will disable auto-registration
Real time level monitoring stops scan if disrupted
Notes: Discuss best practices for Trade show during the presentation.

## Slide 21: Simple - Compact and Portable
5.8 kg with battery
Scanner Dimensions: 178 mm W x 350 mm H x 170 mm D
Custom backpack
  Easy transport at the job site
  Carry-on compliant for most airlines
Custom Gitzo Series 3 Tripod
  Lightweight and easy transport
Quick release adapter
Perfect size for stability and transportability

## Slide 22: Professional - Scanner Reliability
Operating temperature
  –20°C to +50°C (–4°F to 122°F)
Rugged, durable and trusted
  IP55 (Ingress Protection for dust and water jet)
  Enclosed scanning mirror is safe, clean and robust
Advanced deflection drive technology
  Highly reliable, long lifetime
  Low friction and power consumption
  No noise…you can’t hear it running!
Industry leading, 2-year Trimble Optical Warranty
Made in Jena, Germany
Instrument built for demanding applications

## Slide 23: Workflow Flexibility
Workflow options
Tablet - Connected to Perspective
  Data syncs back to tablet and is registered in real time
Push Button - Connected
  Scanner uses last scan settings
  Data syncs back to tablet and is registered in real time
Push Button - Disconnected
  Scanner uses last scan settings
  Data imported later at user convenience and registered automatically in sequence

## Slide 24: Professional - Seamless Data Integration
Or any other software that can import point clouds!

## Slide 25: Professional - Data Integration
Point Cloud Exports
  E57 / LAS (Industry Standard formats)
  RCP (Autodesk, including ReCap, Revit, Civil3D, Navisworks)
  POD (Bentley format)
  PTX (Leica)
Trimble Office Software (TZF / TDX)
  Trimble RealWorks
  Trimble Business Center
  Other Trimble solutions - Trimble RealWorks Forensics, Tekla, SketchUp, Trimble EdgeWise

## Slide 26: Trimble RealWorks & TBC Integration
Simple drag + drop Trimble Perspective data files from the Trimble X7 scanner
Support for Perspective’s scan labels + field annotations within existing TRW & TBC features to eliminate learning curve
X7 scan data integrates seamlessly with TRW & TBC’s scanning workflows

## Slide 27: Customer and Application

## Slide 28: Customer Segmentation Overview
New 3D Scanning User
  Needs easy integration into their workflow
  Must provide ROI with small budgets
Trimble Fan….Except Scanning
  Values Trimble’s Legacy of workflow productivity and professional reliability
  Knows the Trimble ecosystem
Existing 3D Scanning User
  Understand scanning ROI
  Looking to expand business capacity
  Established process and data workflows
Simple
Smart
Professional

## Slide 29: Top Applications
Building Construction/Facility Management
Industrial Surveys
Civil Infrastructure
Topographic/General Surveys
Forensics
Utilities
Marine Construction
Underground Mining
Cultural Heritage
Tank Calibration & Inspection

## Slide 30: Building Construction / Facility Management
Survey Services for Buildings. Condo maps, facade elevations or large facility management
Labels to help group assets locations by floors
Annotations to call out specific areas of interest in scan data for office personnel
Ensure all areas are captured with in field registration
Survey grade leveling for accurate floor flatness routines without additional control

## Slide 31: Industrial Surveys
Versatility from small as-builts & retrofits, to large capital projects
Quickly capture complex scenes
Capture difficult objects (dark surfaces, Shiny pipes)
Ensure your data is complete, via registration assist
Increase data processing productivity by annotating (P&ID) labels while in the field

## Slide 32: Civil Infrastructure
When safety and speed are a major concern
Comprehensive fast data capture from a safe setup
  Reduce traffic control burden
  Increase worker safety
Ensure data completeness without site revisits

## Slide 33: Topographic / General Survey
Improved visibility on all projects
Complete site details
Fast data collection
Survey-grade leveling for accurate topo on assumed project coordinates without targets or extra control

## Slide 34: Forensics
Improved visibility on all projects
Complete scene visibility
Evidence annotations for critical markets
Measurements in the field
Fast setup times including image capture to quickly open highways
Fully Registered in the field

## Slide 35: Additional Application Examples
Marine Construction
Cultural Heritage
Utilities

## Slide 36: Trimble Scanning Portfolio

## Slide 37: Trimble X7 Positioning Statement
High-speed 3D laser scanning system with new innovations to simplify adoption, increase efficiency and provide confidence in the field.
Trimble Registration Assist for Simple and fast in-field scan registration
Trimble X-Drive for SMART on the fly calibration to help ensure data Quality on every scan
Professional instrument quality you can trust with IP55 and Industry leading 2 year warranty

## Slide 38: Trimble TX8 Positioning Statement
Ultra-high-speed 3D laser scanner with no compromise on range & accuracy to deliver unsurpassed performance and versatility
Trimble Lightning technology for ultra-high speed & high precision over full scan range
Best value for high end performance
Standard and extended range models
Flexibility to address a wider range of projects

## Slide 39: Trimble TX6 Positioning Statement
High-speed 3D laser scanner with best value-for-money on the market to deliver essential performance and scan quality
Trimble Lightning technology for high speed & precision over full scan range
Essential performance for small to medium size projects
Notes: The TX6 provides the best value for the money to deliver essential performance and scan quality.
You get high speed and precision over the full scan range with the necessary performance for small to mid-size projects.

## Slide 40: Trimble SX10 Positioning Statement
The most INNOVATIVE surveying solution we’ve ever engineered. The SX10 truly merges high speed 3D scanning, high accuracy surveying measurements and enhanced imaging capability into one seamless solution. This solution will Transform the way surveyors work without requiring them to change the way they work.
Trimble Lightning 3DM technology for high speed and high precision for all your measurement styles (DR, prism and scanning)
Best Range - 600m +
Survey workflow or scanning workflow
Flexibility to address a wider range of projects

## Slide 41: The Right Solution for the Right Application

## Slide 42
Compare | X7 | TX6 | TX8 | SX10 | RTC360 | BLK360 | FOCUS S
Range | 80m | 120m | 340m | 600m | 130m | 60m | 70m, 150m, 350m
3D Point Acc (at 20m) | 3.5mm | 3mm | 3mm | 2mm | 2.9mm | 8mm | 3.5mm
Leveling Accuracy | 3” | 1” | 1” | 0.5” | 3’ = 180” | ND (180”) | 19”
Typical Scan Duration | 4mns | 3mns | 2mns | 6mns | 1mn | 2mns | 6mns
Imaging | 3x10MP, 1mn | 10MP, 1mn | 10MP, 1mn | 3x5MP, 3mns | 3x13MP, 1mn | 3x5MP, 2mns | 8MP, 3mns
Weight (incl. battery) | 5.8kg | 11.2kg | 11.2kg | 7.8kg | 6.03kg | 1kg | 4.2kg
Calibration | Automatic calibration | Annual Service | Annual Service | Manual field calibration Biannual Service | Annual Service | Annual Service | Annual Service
Typical Workflow | Full in-field registration | Target-based or cloud-based registration | Target-based or cloud-based registration | Survey | In-field Pre-registration | Target-based or cloud-based registration | On-site Registration with laptop
Field Software | Trimble Perspective | Onboard Remote Control | Onboard Remote Control | Trimble Access | Onboard FIELD360 | FIELD360 | Onboard
Standard Warranty | 2 Year | 1 Year | 1 Year | 2 Year | 1 Year | 1 Year | 1 Year
Scan Angular Accuracy | 21” | 17” | 17” | 5” | 18” | ND (66”) | 19” *
Range Accuracy | 2mm | <2mm | <2mm | 2mm+1.5ppm | 1mm+10ppm | 7mm | 1mm
Range Noise | <3mm@40m | <2mm@120m | <1mm@80m | <1.5mm@200m | 0.5mm@20m | Not Disclosed | 0.3mm *
Scan Speed | Up to 500kHz | 500kHz | 1MHz | 26.6kHz | 2MHz | 360kHz | 976kHz
IP Rating | IP55 | IP54 | IP54 | IP55 | IP54 | No | IP54
Temp Range | -20;+50 | 0:40 | 0;40 | -20;+50 | -5;+40 | 5;40 | 5;40

## Slide 43: Sales Information

## Slide 44: Trimble X7 Instrument Pack - PN X7-100-00
Shipped in transportation case
  Trimble X7 Scanner
  3 x Standard Trimble Optical Batteries
  Quick Start Guide, RID, CoC, Warranty Cards
  SD Card Reader
  Standard SD Card (32GB SDHC)
  Cleaning Cloths
  USB Cable
Regional battery chargers ordered separately
  Dual Slot Battery Charger
  Power Supply for Charger
  Power Supply Cable for Charger
Notes: Read from slide
Call out the product bulletin as a place to find more information

## Slide 45: Key Trimble X7 Accessories
Trimble X7 Backpack
  Part Number X7-BP-01
  Custom foam insert
    Trimble X7, 3 batteries and charger
  Front pocket
    T10 Tablet, shoulder strap, extra batteries
  Side pockets for power supplies and cables
  Side straps to hold tripod
  Airline carry-on compatible for most aircraft

## Slide 46: Key Trimble X7 Accessories
Gitzo Series 3 Tripod with Bell Connector
  Part Number 90573-TR
Quick Release Adapter
  Part Number 90573-QR
  Optional accessory for 90573-TR
  Quick Release attaches to X7 base
  Custom head attaches to Gitzo Series 3
Notes: Read from slide
Call out the product bulletin as a place to find more information

## Slide 47: Trimble Installation Manager
Both Instrument Firmware and Software Installation
Instrument FW
Perspective SW

## Slide 48: Thank You