## Slide 1: GEDO NovaTrack. Introduction Trimble Geospatial Track Survey & Scanning
Linas Maciulevicius | Trimble Geospatial
FEBRUARY 13, 2023
V.2.2.2

## Slide 2: AGENDA
Short intro into GEDO NovaTrack software
Key features
Standard workflows & special case
Live demo
Reference & Support information
Questions

## Slide 3: Goals within track maintenance and renewal
Reduction of maintenance/renewal cycles
Avoid issues with the clearances to the structures
Increase in life of track infrastructure
Track improvements by detecting geometry irregularities
Always known the initial track position
Increase construction asset utilization
Route re-construction
New track layouts
Plain line renewal
S&C renewal and refurbishment
Maintenance works
Sidings renewals / maintenance
Control by Design

## Slide 4: Typical issues with alignment data
Challenges with track design alignments:
Design alignment data is not available or partial
Transition tangents are moved due to the relative tamping process
Both vertical and horizontal radii are drifted from the original design
Cant alignment is off from design
No control of clearances before and after re-alignment
Track alignments:
Initial design
Existing

## Slide 5: Consequences of bad* track maintenance
Source: UIC
* - relative

## Slide 6: What is Trimble GEDO NovaTrack ?
Trimble GEDO NovaTrack – software for analysis of existing track geometry and approximation with best fit design alignment geometry elements
Primary applications
  Create design alignment data for track maintenance (design tamping)
  Evaluation of existing track geometry parameters
  Checking historical alignment data against existing track position
  Adjustment of old design alignment to match with existing track

## Slide 7: GEDO NovaTrack - finding best-fit alignment solution
Key functionality and features:
Automatic alignment fitting based on existing track measurement data
Curvature prediction using 1/R curvature and Direction Analysis
Clearance info during alignment adjustment process
Calculation of design speed and cant
Check alignment conformity against design regulations

## Slide 8: GEDO NovaTrack workflows - from measurement to a specific application Trimble Geospatial Track Survey & Scanning
V.2.2.2
02

## Slide 9: Data flow - from field to rail specific application
GEDO Scan Office
Dynamic clearance analysis
Structures & Platforms
OHL lines
GEDO Office
Machine Control
Deformation Monitoring
Tamping/QA
Processing
Measurements/Scan
Analysis applications
Re-Alignment
Production applications
CAD/BIM Software
Detail track design
GEDO NovaTrack
Best-fit alignment processing
HA/VA/CANT/SPEED
GEDO REC
GEDO IMS
GEDO VORSYS
GEDO Office
Measured existing tracks
Trimble MX9/MX50 (Mobile Mapping)
GEDO IMS SCAN
GEDO Scan Office
Measured tracks
Extracted existing tracks
Topographical objects
TA Track
Gauge Survey
TBC
Measured existing track (rail) points

## Slide 10: Alignment processing workflows
Recommended workflows for track re-alignment
.GTD
.TDT
.HDT
.UDT
Complete
re-alignment
HA/VA method
Import .GTD track data
Semi-automatic or automatic HA fitting
Adjustment HA elements. Reduction HA offsets
Automatic VA fitting, reduction of VA offsets
Cant and speed calculation (optional)
Design alignment export to .TDT/.HDT/.UDT files
1
2
3
4
5
6
A
Horizontal
re-alignment
HA method
Import .GTD track data
Semi-automatic or automatic HA fitting
Adjustment HA elements. Reduction HA offsets
Design alignment output to .TDT file
1
2
3
4
B
Vertical
re-alignment
VA method
Import .GTD track data
Automatic VA fitting
Design alignment output to .HDT file
1
2
3
C
Verification of alignment
Verification method
Import .GTD track data
Import design alignment
Check HA/VA offsets and compliance with rules
1
2
3
D

## Slide 11: Track survey data input. Option #1
Input measurement data:
Track measurements in the GEDO Track Data .GTD format:
  Center line (X, Y)
  Elevation (H, lower rail)
  Measured Cant

## Slide 12: Track survey data input. Option #1
Data input from track survey and scan:
Measured track trajectory in .GTD format:
  point name and code
  center line (X, Y, H)
  measured gauge (meters)
  measured inclination (radians)

## Slide 13: Track survey data input. Option #2
Data input from other track survey sources:
Track points in .XML (.cgPoint) or .CSV format:
  point name and code (code for left/right rail or axis)
  point coordinates (left/right rail or axis)
  coordinate precision 5 decimals or more

## Slide 14: Requirements for track measurement data (input)
Input data specification:
Interval between measured points
  depending on track quality/complexity/application: 0.5 – 3 m
Measured point coverage:
  measurements must start/end in a straight or radii element (at least 50 m)
  measurements should not start/end in the transition
  the gaps are allowed in the measurement data

## Slide 15: Workflow. Step 1. Data input.
Import of measured track data (.GTD)
Horizontal view
Vertical view
Cant diagram view

## Slide 16: Workflow. Step 2. Selecting calculation settings
Selecting chainage range: from – to chainage
Selecting calculation profile (based on application or track type)
Selecting alignment calc. scope: HA/VA, HA, VA or Validation

## Slide 17: Workflow. Step 3. Automatic alignment fitting
Point approximation with alignment elements
Novatrack 3.0
´Pre-design´
Better automatic prediction
Consistent geometry
Aimed for re-construction
1
2
3
A
Regression w/ Transitions
´Smoothing´
Follows existing track
Erratic combinations of elements
Suitable smoothing tamping
1
2
3
B

## Slide 18: Workflow. Step 4. Automatic fitting result
Design alignment result after automatic alignment fitting
SL
TC
C
TC
SL
TC
C
TC
C
SL
Speed/ Cant diagram view
VA alignment offsets
HA alignment offsets
1/R curvature band
Straight line
Transition
Radius/Arc
Invalid fitting

## Slide 19: Workflow. Step 5. Semi-automatic alignment fitting
Using HA curvature/direction analysis diagram:
  to adjust proposed HA alignment configuration
  to set preliminar element configuration & tangent point positions
1/R curvature analysis
Direction change analysis
Straight line (A)
Transition
Radius/Arc (A)
Invalid fitting
Preliminary tangent location

## Slide 20: Workflow. Step 5. Semi-automatic alignment fitting
Adjusting HA alignment configuration in Analysis Diagram
Precise HA/VA editing in order to reduce offsets

## Slide 21: Workflow. Step 6. HA alignment fine-tunning
Adjusting HA elements to minimize horizontal offsets:
  direct element editing using parametric data
Offset diagrams
Analysis diagram
Horizontal view
Straight line (A)
Transition
Radius/Arc

## Slide 22: Workflow. Step 7. VA alignment establishment
Establishment and adjust of VA elements :
  draft VA alignment smoothing using calculation profile setting
  VA element parametric editing to minimise vertical offsets
Straight line (A)
Radius/Arc (A)
Calculation profile settings

## Slide 23: Workflow. Step 8. Calculate design Cant
Calculate design Cant using one of the available options:
  Cant calculated based on user profile settings
  Cant calculated as an avarage of measured cant
Cant based on average existing cant
Cant based on user profile
Existing cant
Design cant
Existing cant
Design cant

## Slide 24: Design speed & cant calculation options
Cant averaging and based on measured cant
Cant and speed based on the rule settings
Speed/cant calculation for individual elements

## Slide 25: Workflow. Step 9. Adding supportive map information
Optionally import an external track or map data
  supported format: .GTD, .DXF, .CSV and .LandXML
  available tooltip information: offsets, chainage, layer code

## Slide 26: Data exchange
Supported file formats

## Slide 27: GEDO NovaTrack Live
Live software demonstration
03

## Slide 28: Questions?

## Slide 29
Thank you!
February 13, 2023